## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Simulation of Bragg Peak in Ion Beam Therapy
Petrus Canisius Astuto Santosa, Pasquale Serrao, Anna Simeone,
Alessia Zannino, Bianca Zocco
Milan, 6th June 2024
Study of Different Parameters of Simulation

## Slide 2: Hadrontherapy
Hadrontherapy is a form of radiotherapy for the treatment and cure of tumours.
Unlike traditional radiotherapy based on X-rays or electrons, hadrontherapy involves the use of proton and carbon ions.
(def. By CERN)

## Slide 3: Simulation
CATANA setup implemented in Geant4
Default set-up:
10000 particles
Energy of 60 MeV
Energy standard deviation 0.0 MeV
Simulation of the ion (proton) beam facility in Catania for eye tumor treatment
Phantom material water
Phantom dimension 40 cm x 40 cm x 40 cm
Detector dimension 4 cm x 4 cm x 4 cm
DETECTOR
Detector: 400 slices of 0.1 mm

## Slide 4: Materials
Different materials
Different depth of the Bragg Peak
Lower material density
Deeper peak
 | Adipose tissue | Water | Brain | Eyelens | Compact bone
Bragg peak position [mm] | 27,4 | 27,1 | 25,8 | 25,3 | 15,7
Material density [gr/] | 0,95 | 1 | 1,05 | 1,07 | 1,85
 | Adipose tissue | Water | Brain | Eyelens | Compact bone
Bragg peak position [mm] | 27,4 | 27,1 | 25,8 | 25,3 | 15,7
 | 0,95 | 1 | 1,05 | 1,07 | 1,85
Chart: Materials

## Slide 5: Number of particles
Chart: Biological dose for different number of particles
Chart: RBE @ peak vs #particles
| 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000
 | 3.1586 | 3.1381 | 2.8076 | 2.8302 | 2.5312 | 2.509 | 2.2682
The relative biological effectiveness (RBE) is defined as the ratio between x-ray and particle doses required to cause the same effect in terms of Survival
Total dose:
Sum of the dose from each particle;
Increasing number of particles:
Decreasing RBE at peak;
N° of particles

## Slide 6: Number of particles
Chart: Physical vs biological dose
| 10000 | 20000 | 30000 | 40000 | 50000 | 60000 | 70000
Physical dose | 1.1561 | 2.0484 | 3.0494 | 3.9421 | 4.8646 | 5.8613 | 6.9194
Biological dose | 2.2996 | 3.5251 | 4.5803 | 5.3815 | 6.1687 | 6.9655 | 7.6681
BIOLOGICAL DOSE
=
RBE * PHYSICAL DOSE
Physical dose peak amplitude ~ linearly dependent on the number of particles;
Biological dose shows a gradual decrease of the slope;
Chart: Comparison between SLOPES
| 10k-20k | 20k-30k | 30k-40k | 40k-50k | 50k-60k | 60k-70k
Biological | 0.00012255 | 0.00010552 | 8.0125e-05 | 7.872e-05 | 7.9676e-05 | 7.0263e-05
Physical | 8.9237e-05 | 0.0001001 | 8.9268e-05 | 9.2247e-05 | 9.9667e-05 | 0.00010581

## Slide 7: Energies
Chart: Different energies
65 MeV | 0.39893 | 0.40799 | 0.44162 | 0.38651 | 0.40237 | 0.42551 | 0.38377
Different energies Different depth of the Bragg Peak;
Linear relationship between energy and peak depth;
Chart: Bragg peak position
| 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69
Depth [mm] | 27 | 27.9 | 28.7 | 29.6 | 30.8 | 31.7 | 32.6 | 33.8 | 34.5 | 35.6
Chart: 
| 60-61 | 61-62 | 62-63 | 63-64 | 64-65 | 65-66 | 66-67 | 67-68 | 68-69
Slope | 0.9 | 0.8 | 0.9 | 1.2 | 0.9 | 0.9 | 1.2 | 0.7 | 1.1

## Slide 8: Energy Standard Deviations Range
Ideal case: SD of 0 MeV;
Under SD of 1 MeV: at least 80% of the expected dose with 0 MeV of SD
Chart: Comparison of Energy Standard Deviations
Chart: Relative dose @ peak vs #Std Dev
| 0 | 0.5 | 1 | 1.5 | 2
 | 100 | 97.0627 | 82.2817 | 64.6941 | 61.7967

## Slide 9: SOBP
Analytical reconstruction of the SOBP (S. Bijan Jia et. al. (2016) ):
Assigning weight to the 10 bragg peaks (of same amplitude and different position);
Possible real implementation retrieving the number of particles to use for each energy according to the computed weight;
Chart: Different energies
65 MeV | 0.39893 | 0.40799 | 0.44162 | 0.38651 | 0.40237 | 0.42551 | 0.38377
Chart: SOBP

## Slide 10: Detector shift: DEPTH SHIFT
Chart: DOSE PEAK @ Different shifts
| 0 | 5 | 10 | 15 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 2.1379 | 2.2789 | 2.1909 | 1.9582 | 2.0141 | 1.9878 | 2.1821 | 2.2437 | 2.3014 | 2.0905 | 2.4174 | 1.9217 | 0.12294
Depth shift: no difference in the peak amplitude
DEPTH SHIFT:
Limit distance for dose deposition

## Slide 11: Detector shift: TRANSVERSAL SHIFT
Chart: LATERAL SHIFT: Biological Dose
Increasing transversal shift:
Lower dose;
Higher randomness in the shape of the curve;
TRANSVERSAL
SHIFT:
Chart: Dose PEAK @ DIFFERENT SHIFTS
| 0 | 4 | 8 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36
 | 2.1379 | 2.353 | 2.2398 | 2.1355 | 2.2677 | 2.2068 | 1.8795 | 1.4356 | 1.0501 | 0.47969 | 0.4064 | 0.076415 | 0.10781 | 0.066295 | 0.078725 | 0

## Slide 12: Healthy VS tumoral cell
Chart: Survivance Fraction Comparison
Chart: Biological Dose Comparison
U87: Tumoral Cells (Glioma)
AG01522: Healthy Fibroblasts
@ Peak:
U87: higher Biological Dose
AG01522: lower Survivance Fraction
Entity of DNA damage is cell-dependent

## Slide 13: Effect on healthy tissues
Transition Zone:
Possible movements of the tumor: higher efficiency until the transition zone (d~15 mm)
Healthy tissue surrounding the tumor: higher risk of damage until the end of the transition zone
(d~ 25 mm)
Chart: Survivance @ Peak in function of radial distance
| 0 | 4 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36
U87 | 0.60086 | 0.55375 | 0.57846 | 0.60137 | 0.57237 | 0.5857 | 0.6579 | 0.7546 | 0.83387 | 0.93559 | 0.94685 | 0.99128 | 0.98752 | 0.99472 | 0.99101 | 0.9788 | 1
AG01522 | 0.38063 | 0.35602 | 0.36767 | 0.36842 | 0.36612 | 0.37072 | 0.43798 | 0.50213 | 0.61574 | 0.64551 | 0.85006 | 0.90934 | 0.97664 | 0.9868 | 0.98575 | 0.96761 | 1
Chart: Dose (bio) @ peak in function of radial distance
| 0 | 4 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36
AG01522 | 1.5226 | 1.6136 | 1.5699 | 1.5672 | 1.5757 | 1.5587 | 1.3267 | 1.1293 | 0.8207 | 0.74658 | 0.29111 | 0.17258 | 0.043561 | 0.02454 | 0.026501 | 0.060546 | 0
U87 | 2.1379 | 2.353 | 2.2393 | 2.1355 | 2.2677 | 2.2068 | 1.8795 | 1.4356 | 1.0501 | 0.47969 | 0.4064 | 0.076415 | 0.10781 | 0.066295 | 0.0078725 | 0 | 0
Tumor
Healthy Tissue
Center of the Beam
d
Simulations Real case

## Slide 14: Conclusions
PERSONALIZATION OF THERAPY:
Changing the number of particles to modulate the dose deposition
Keeping the standard deviation of the energy the lowest possible
Retrieving acceptable range of movement according to tumor dimensions
Modulating energy to shift the bragg peak position
lllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllllll

## Slide 15: References
https://fondazionecnao.it/en/hadrontherapy/what-is-hadrontherapy (definition of hadrontherapy and how it works)
Cirrone et al.,(2011). Hadrontherapy: a Geant4-Based Tool for Proton/Ion-Therapy Studies. In Progress in NUCLEAR SCIENCE and TECHNOLOGY (Vol. 2).
Cirrone et al.,(2005). Implementation of a new Monte Carlo - GEANT4 simulation tool for the development of a proton therapy beam line and verification of the related dose distributions. IEEE Transactions on Nuclear Science, 52(1 I), 262–265.

## Slide 16: References
Cirrone et al.,(2004). A 62 MeV Proton beam for the treatment of ocular melanoma at Laboratori Nazionali del Sud-INFN (CATANIA).
Chaudhary, et al.,(2014). Relative biological effectiveness variation along monoenergetic and modulated Bragg peaks of a 62-MeV therapeutic proton beam: A preclinical assessment. International Journal of Radiation Oncology Biology Physics, 90(1), 27–35.
S. Bijan Jia et al. Designing a range modulator wheel to spread-out the Bragg peak for a passive proton therapy facility, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, Volume 806, 2016, Pages 101-108, ISSN 0168-9002.
https://www.lnf.infn.it/media/notiziario/not11/Art.12.pdf

## Slide 17: References
Paganetti, H. (2009), MO-SAM-BRB-01: Biological Aspects of Heavy Charged Particle Radiation Therapy. Med. Phys., 36: 2685-2685
Schilling I, Bäcker CM, Bäumer C, Behrends C, Hötting M, Hohmann J, Kröninger K, Timmermann B, Weingarten J. Measuring the Beam Energy in Proton Therapy Facilities Using ATLAS IBL Pixel Detectors. Instruments. 2022; 6(4):80.

## Slide 18: Detector shift – X direction
Chart: BIOLOGICAL DOSE (Gy) FOR DIFFERENT SHIFTS - HEALTHY CELLS
Chart: DOSE PEAK FOR DIFFERENT SHIFTS
| 0 | 5 | 10 | 15 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 1.5226 | 1.4379 | 1.3543 | 1.5221 | 1.366 | 1.5775 | 1.7993 | 1.3455 | 1.4575 | 1.4999 | 1.604 | 1.4138 | 0.030958
Chart: BIOLOGICAL DOSE (Gy) FOR DIFFERENT SHIFTS - TUMORAL CELLS
Chart: DOSE PEAK FOR DIFFERENT SHIFTS
| 0 | 5 | 10 | 15 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28
 | 2.1379 | 2.2789 | 2.1909 | 1.9582 | 2.0141 | 1.9878 | 2.1821 | 2.2437 | 2.3014 | 2.0905 | 2.4174 | 1.9217 | 0.12294

## Slide 19: Detector shift: TRANSVERSAL SHIFT
Chart: Dose PEAK @ DIFFERENT SHIFTS
| 0 | 4 | 8 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36
 | 2.1379 | 2.353 | 2.2398 | 2.1355 | 2.2677 | 2.2068 | 1.8795 | 1.4356 | 1.0501 | 0.47969 | 0.4064 | 0.076415 | 0.10781 | 0.066295 | 0.078725 | 0
Chart: LATERAL SHIFT: Biological Dose
Chart: SHIFT = 0 mm
Chart: SHIFT = 28 mm
Increasing transversal shift:
Lower dose
Higher randomness in the shape of the curve
Notes: Moving on the transversal shift